## Slide 1
Zener Diodes
Voltage Regulation

## Slide 2
Zener Diodes
  Operates in reverse bias
  If in parallel with a load, can keep constant voltage
Cathode
Anode

## Slide 3
Zener Diodes
  IS is between Imin and Imax
    Below min – does not work
    Above max – will work for a while then burn up
RS
RL
E

## Slide 4
Zener Diodes
  Let:
  VZ = 5.1V
  RS = 240Ω
  RL = 250Ω
  IZK = 4m A
  IZM = 80m A
  VRS = 20 – 5.1
  = 14.9V
  VRL = 5.1V
RS
RL
E

## Slide 5
Zener Diodes
  E = 20V
  VZ = 5.1V
  RS = 240Ω
  RL = 250Ω
  IZK = 4m A
  IZM = 80m A
  IRL = 14.9/250
  = 20.4m A
  IT = 14.9/240
  = 62.1m A
  IZ = IT – IL
  = 62.m – 20.4m
  = 41.7mA
RS
RL
E

## Slide 6
Zener Diodes
  IZK < IZ < IZM
  Power Dissipated
  Load Regulation